## Slide 1
Adjust pedal unit angle
Adjust spring tension
Adjust damper levels
Remove the two bolts and 4 washers
Adjust travel range
Step 2: Loosen the 2 bolts on the sides and move the bottom blue bump stop up or down, find your preferred recline angle then tighten the bolts
Step 1: Twist the spring cap to a high position
Step 3: Loosen the 4 bolts on both sides and move the top blue bump stop forward or backward to find your preferred pedal travel range.
Adjust the height of the pedal face
Choose a suitable pedal height, then tighten the bolts.
Loosen the 4 screws on the sides behind the pedal face
Option 1: 2.5mm spring + 2 elastomers
Option 2: 3mm spring + 2 elastomers
Option 3: 2.5mm spring + 3mm spring + 1 elastomer
Twist the spring tension adjustment cap further to the front to reduce spring tension and further to the back to increase spring tension
3 recommended combos include:
Remove the bolts, change to a suitable elastomer combo, reinstall and tighten
1
2
3
4
Select the suitable angle. The manufacture provides 7 angle adjustment holes to set your pedal angle. Tighten the bolts to secure the angle brackets to the Brake unit.
0º
-3º
-6º
3º
6º
9º
12º
Twist the end of the damper unit so that the white dot lines up with a number. 1 being the easiest to depress the pedal and 8 being the hardest to depress the pedal