## Slide 1
Choose a suitable pedal height, then tighten the bolts.
Adjust pedal unit angle
Remove the two bolts and 4 washers
Loosen the 4 screws on the sides behind the pedal face
Adjust the height of the pedal face
Adjust travel range
Step 2: Loosen the 2 bolts on the sides and move the bottom blue bump stop up or down, find your preferred recline angle then tighten the bolts
Step 1: Twist the spring cap to a high position
Step 3: Loosen the 4 bolts on both sides and move the top blue bump stop forward or backward to find your preferred pedal travel range.
Adjust spring tension
Twist the spring tension adjustment cap further to the front to reduce spring tension and further to the back to increase spring tension
Adjust damper levels
Twist the end of the damper unit so that the white dot lines up with a number. 1 being the easiest to depress the pedal and 8 being the hardest to depress the pedal
1
2
3
4
Select the suitable angle. The manufacture provides 7 angle adjustment holes to set your pedal angle. Tighten the bolts to secure the angle brackets to the Throttle unit.
0º
-3º
-6º
3º
6º
9º
12º
THROTTLE

## Slide 2
Adjust pedal unit angle
Adjust spring tension
Adjust damper levels
Remove the two bolts and 4 washers
Adjust travel range
Step 2: Loosen the 2 bolts on the sides and move the bottom blue bump stop up or down, find your preferred recline angle then tighten the bolts
Step 1: Twist the spring cap to a high position
Step 3: Loosen the 4 bolts on both sides and move the top blue bump stop forward or backward to find your preferred pedal travel range.
Adjust the height of the pedal face
Choose a suitable pedal height, then tighten the bolts.
Loosen the 4 screws on the sides behind the pedal face
Option 1: 2.5mm spring + 2 elastomers
Option 2: 3mm spring + 2 elastomers
Option 3: 2.5mm spring + 3mm spring + 1 elastomer
Twist the spring tension adjustment cap further to the front to reduce spring tension and further to the back to increase spring tension
3 recommended combos include:
Remove the bolts, change to a suitable elastomer combo, reinstall and tighten
1
2
3
4
Select the suitable angle. The manufacture provides 7 angle adjustment holes to set your pedal angle. Tighten the bolts to secure the angle brackets to the Brake unit.
0º
-3º
-6º
3º
6º
9º
12º
Twist the end of the damper unit so that the white dot lines up with a number. 1 being the easiest to depress the pedal and 8 being the hardest to depress the pedal
BRAKE

## Slide 3
Adjust pedal unit angle
Adjust the height of the pedal face
Adjust travel range
Adjust spring tension
Adjust damper levels
Remove the two bolts and 4 washers
Step 2: Loosen the 2 bolts on the sides and move the bottom blue bump stop up or down, find your preferred recline angle then tighten the bolts
Step 1: Twist the spring cap to a high position
Step 3: Loosen the 4 bolts on both sides and move the top blue bump stop forward or backward to find your preferred pedal travel range.
Choose a suitable pedal height, then tighten the bolts.
Loosen the 4 screws on the sides behind the pedal face
Twist the spring tension adjustment cap further to the front to reduce spring tension and further to the back to increase spring tension
1
2
3
4
Select the suitable angle. The manufacture provides 7 angle adjustment holes to set your pedal angle. Tighten the bolts to secure the angle brackets to the Clutch unit.
0º
-3º
-6º
3º
6º
9º
12º
Twist the end of the damper unit so that the white dot lines up with a number. 1 being the easiest to depress the pedal and 8 being the hardest to depress the pedal
CLUTCH