## Slide 1
Step 1: Remove the elastomer stack
Step 2: Choose a suitable combination of springs and elastomers
Step 3: Remove the bumpstop
Step 5: Adjust the damper
Step 6: Tighten the damper and remove the spacer
Step 7: Re-install the bumpstop.
Step 4: Install the damper
Step 8: Re-install the elastomer stack
Step 9: Adjust the height of the pedal face
Option 1 stiffest: 2.5mm spring + 2 elastomers
Option 2 stiffer: 3mm spring + 2 elastomers
Option 3 soft: 2.5mm spring + 3mm spring + 1 elastomer
Step 6.2: Remove the spacer.
Step 6.1: Fix the damper in place by screwing in the plastic- headed grub screw
Step 5.1: Insert the 3D printed spacer.
Step 5.2: Tighten the whole damper until it touches the spacer
Twist the damper into the large threaded hole
Insert the piston shaft into the hole and tighten with the grub screw
Damper
3D printed spacer
M5x6 flat-headed grub screw
M5x4 plastic-headed grub screw
Parts needed to install the damper to your Brake unit
Reinstall the stack and adjust the preload to your liking.
Remove the 2 hex bolts on the sides, push the pedal arm backwards and slide the blue bumpstop downwards
3 combinations are recommended but feel free to mix and match to find the perfect combo for you: